## Slide 1
Simple Stopwatch
Simulator
Interrupt-driven timing with S2 assembly
00:00.00
Hardware Design and Implementation
Notes: This project simulates a stopwatch on the course S2 CPU. The goal is to demonstrate how timer and button interrupts control elapsed time and lap recording. S2 assembly owns the stopwatch logic. Python runs the simulator and provides its input and display. The timer shown on this cover is the initial display, not a captured test result.
Project sources:
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\README.md
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\stopwatch.txt

## Slide 2
What the project does
02
Measure elapsed time and record laps while the timer runs.
S
Start / Pause
Start, pause, or resume the current time.
L
Save lap
Save a timestamp and lap duration. Maximum 10 laps.
R
Reset
Stop the timer, return to zero, and clear all laps.
Display format: minutes : seconds . hundredths
Notes: The user can click the buttons or use S, L, and R while the simulator window has focus. A lap saves both the cumulative elapsed time and the duration since the previous lap. Timing continues after a lap. A lap request while paused is ignored. Pausing preserves time and previous laps, and paused time is excluded after resuming. Records remain in simulated RAM until reset or closing the window.
Project sources:
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\README.md
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\simulator.py
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\stopwatch.txt

## Slide 3
Planning the system diagram
03
Separate the assembly logic from Python input and display.
Simulated timer
1,000 cycles / tick
Python buttons
Command + IRQ2
INT0 handler
Increment if running
INT2 handler
Start, lap, reset
RAM
Elapsed ticks
RAM
State and laps
Python
display
Reads RAM
One timer tick displays as 0.01 seconds.
Notes: Explain the plan from left to right. Timer0 raises IRQ0 every 1,000 simulated CPU cycles. The INT0 assembly handler adds a tick only while running. Python buttons write a command to mailbox address 1104 and request IRQ2. The INT2 assembly handler changes running state, saves laps, or resets memory. The window reads RAM and formats it. The diagram groups RAM by purpose, not separate physical memories. Button reset also clears elapsed ticks. Each ISR saves and restores r0-r15 and returns with RETI. IRQ0 has priority when both requests are pending. These interrupts belong to the simulated CPU, not a physical microcontroller.
Project sources:
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\README.md
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\stopwatch.txt
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\simulator.py

## Slide 4
Implementation
04
01
Initialize the CPU
Set the interrupt vectors, stack, timer, and memory.
02
Write the S2 handlers
Update elapsed ticks and save lap values in RAM.
03
Build and verify
Assemble the program, run tests, then open the GUI.
Run in the stopwatch folder
python build.py
python test_stopwatch.py
python simulator.py
Lap duration = current timestamp - previous timestamp
Notes: First initialize r29 to 3000, install the timer ISR at vector 1000 and button ISR at vector 1002, initialize state, and enable IRQ0 and IRQ2. The main loop counts normal execution passes and waits with WFI. The timer ISR checks the running flag. The button ISR dispatches command 1 for toggle, 2 for lap, and 3 for reset. A lap writes the cumulative timestamp to addresses 1200-1209 and its duration to 1220-1229. trap r29 #15 saves r0-r15, trap r29 #16 restores them, and RETI returns to the interrupted program. Example lap timestamps of 00:03.20 and 00:07.85 give a second lap duration of 00:04.65. The listed commands are the project workflow. Do not describe the tests as passed unless you have just run them.
Project sources:
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\stopwatch.txt
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\README.md
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\PRESENTATION.md
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\test_stopwatch.py

## Slide 5
Problems and solutions
05
Problem / limit | Solution or handling
Console input blocks execution | Use a Python adapter so the CPU keeps running while the user presses buttons.
RAM has only 10 lap slots | Check capacity before saving. Keep existing laps and use Reset to clear memory.
Simulation can lag real time | Treat 0.01 s ticks as simulated time. Host load can affect the display pace.
The project demonstrates timer and button interrupts in S2 assembly.
Notes: The original course monitor blocks when reading input and limits each run. The Python adapter replaces that interaction while retaining the original CPU decoder, timer, and interrupt dispatcher. Memory holds ten lap records. An eleventh request produces a full-memory message without overwriting earlier records, and timing continues. The displayed tick is 0.01 seconds, but it represents simulated CPU cycles. Host scheduling or heavy load can introduce lag. Present this as a demonstration of interrupts rather than a calibrated stopwatch. These are documented design constraints and handling choices, not claims about newly measured failures. End by demonstrating Start, Lap, Pause, Resume, and Reset.
Project sources:
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\README.md
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\PRESENTATION.md
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\simulator.py
D:\CEDT\Hardware-Design-and-Implementation\mid-project\stopwatch\stopwatch.txt